## Slide 1: Exploring Containerization for Protecting Unmanned Robotic Vehicles
Chidera Okoro
cjokoro@shockers.wichita.edu
Hasan Monowar
monowar.hasan@wichita.edu

## Slide 2: Robotic Vehicles (RVs)
Surveillance
Communication
Delivery
Agriculture
Manufacturing
Applications

## Slide 3
Traditional robotic vehicles:
  Custom hardware
  Closed-source software
  Not interconnected
Modern robotic vehicles:
  Off-the-shelf (COTS) components
  Open-source software
  More interconnected  Internet
RV Security?
Larger attack surface!

## Slide 4
RV Security?

## Slide 5
Operating System
RV Application
Vanilla Robotic Systems
RV malfunction
No way to control what goes in and out of application
System may crash
  Fatalities among humans
  Destruction to surrounding environment
malicious attack
Can we do better?

## Slide 6
Attack Model
RV application can be compromised
  No specific assumptions on how the attacker compromise
  bugs, vulnerabilities, social engineering, remote update
OS is trusted
Hardware attacks are not considered
Adversary Model
RV Hardware
Operating System
RV Application

## Slide 7: Our Approach Sandboxing RV Applications
Containerization
Isolates surrounding environment (sandboxing)
Limits resources
Container
RV Application
Operating System
RV application runs inside the container
Operating system communicates with containers
Container
RV Application
Container
RV Application
Container
RV Application

## Slide 8
Operating System
RV Application
Configuration Manager
Containerization of RV Applications
Monitors the behavior of the application
Able to see what goes in and out of application
We can enforce design time configurations
Container
malicious attack

## Slide 9
Control groups
responsible for managing resource usage
Namespaces
provides isolation of system resources
Ethernet
network interface that is bridged to OS network
Hardware
Operating System
RV Application
Container Runtime
Linux Container (LXD)
Configuration Manager
Containerization of RV Applications

## Slide 10: Experiment Setup
Hardware
  Raspberry Pi 3 Model B
  Navio2 extension board
Software
  Ardupilot Software Version 3
  Linux Container – LXD 4.0
Implementation publicly available:
https://github.com/CPS2RL/rv_security_container.git

## Slide 11
Experiments
Security Analysis and Overhead Analysis
System call
- Implementing an attack that inserts a denied system call into a program
Memory Exhaustion
- Implementing an attack that overcomes the allowed threshold for memory storage
malicious attack
Performance in Execution Time
- Took over 10,000 data points to calculate the mean, standard deviation, 99th percentile, and ECDF
Denial of Service
Performance Overhead
Performance in Memory Usage
- Took over 10,000 data points to calculate the mean, standard deviation, 99th percentile, and ECDF

## Slide 12: Results

## Slide 13: Security Analysis: System Call Access
if(GPS.init(){
GPS.setSensor(1);
}
else{
GPS.setSensor(0);
}
The brk() function is being called and used in our approach.
The brk() function is disabled from being accessed by the container.
When an unauthorized system call is implemented into the program, it results in the change of the execution flow.
Denial of Service
brk();

## Slide 14: Security Analysis: System Call Access Experiment Two
Writing to root-authorized file can cause the ardupilot software to not perform correctly
An attacker can write to a file that changes the implementation of the propeller

## Slide 15: Security Analysis: Memory Exhaustion
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5
Percentage of Memory Used | 1.7 | 3.3 | 4.8 | 6.2 | 7.7 | 9.1 | 10.6 | 12 | 13.5 | 14.9 | 16.3 | 17.9 | 19.2 | 20.8 | 22.2 | 23.7 | 25.1 | 26.6 | 28 | 29.5 | 30.9 | 32.4 | 33.8 | 35.3 | 36.7 | 38.3 | 39.6 | 41.1 | 42.5 | 43.9 | 45.4 | 46.8 | 48.4
Chart: 
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5
Percentage of Memory Used | 5.2 | 6.7 | 8.1 | 9.6 | 11 | 12.5 | 13.8 | 15.3 | 16.7 | 18.1 | 19.5 | 21 | 22.3 | 23.8 | 25.2 | 26.7 | 29.5 | 30.8 | 32.3 | 33.7 | 35.2 | 36.5 | 38 | 39.4 | 40.9 | 42.2 | 43.7 | 45 | 46.5 | 47.9 | 49.2 | 50.7 | 52.1 | 53.5 | 54.9 | 56.4 | 57.7 | 59.2 | 60.6 | 62.1 | 63.4 | 64.9 | 67 | 70.1 | 73
Percentage of Memory Usage
Our Approach
Vanilla
Execution Time in Seconds
Memory Exhaustion
Our Approach
With the use of containerization, the configuration manager can detect the memory leak and prevent the software from a segmentation fault.

## Slide 16: Overhead Analysis Impact on Execution Time
 | Execution Time (microseconds) | 
 | Vanilla | Our Approach
Mean | 29.133 | 31.186
STD. Deviation | 8.868 | 10.673
99th Percentile | 68.206 | 76.023
Our Approach
Vanilla
Empirical Distribution Graph of Ardupilot Barometer Application
ECDF
Execution Time in Microseconds
Chart: 
Chart: 
The overhead of our approach was minimal with only a 1.07x increase in application execution time
Summary:

## Slide 17: Overhead Analysis Impact on Memory Usage
Chart: 
 | Execution Time (kilobytes) | 
 | Vanilla | Our Approach
Mean | 67.302 | 98.522
STD. Deviation | 55.906 | 90.538
99th Percentile | 252 | 252
Chart: 
Kilobytes Used
Our Approach
Vanilla
ECDF
Empirical Distribution Graph of Ardupilot Barometer Memory Usage
The overhead of our approach was minimal with only a 1.46x increase in application execution time
Summary:

## Slide 18: Conclusion
Our research shows the feasibility of using containers for RV applications
Containerization of RV Applications
  Allows to monitor the behavior of the RV application without significant overheads
  Can enforce design time configurations and prevent unauthorized access
Our future research:
  Will explore attacks on other signals (such as I/O, network, and timing anomalies).
  Will also evaluate other autopilot software (e.g., Paparazzi and PX4).

## Slide 19: Thank You!
Questions?